## Slide 1: Reusing and Changing Existing Buildings on Site
Module 1 ¦ Why Lifecycle Matters | Construction · Climate · Resources
Duration | 6 hours

## Slide 2
INSIDE-CoVE
Erasmus+ Centre of Vocational Excellence
Lifecycle & Digital Circularity
EQF 3–5 · Blue Collar
6 hours · 4 sessions
MODULE 1
Why Lifecycle
Matters
IN THIS MODULE
• Construction's resource and carbon footprint
• Linear vs circular economic models
• EU and national policy drivers
• Embodied carbon and five site actions

## Slide 3
MODULE 1
Why
Lifecycle
Matters
6 hours · 4 sessions
Welcome to the module
In the next 6 hours, you'll learn how the buildings we put up — and the materials we use — shape the climate, our resources, and the policies that now shape your job.
01
Learn
The science, the data, and why this matters now
02
Think
Linear vs circular — what you've been doing vs what's needed
03
Act
Five everyday site decisions that change the outcome
2

## Slide 4
MODULE OBJECTIVES
By the end of this module, you will be able to:
01
Describe
the construction sector's resource flows and climate impacts using simple data (tonnes, percentages, CO₂)
02
Distinguish
between linear and circular economy models and give one real construction example of each
03
Identify
at least three EU and national policies that affect site-level decision-making in your trade
04
Explain
what embodied carbon means in plain language and propose three on-site actions that reduce it
INSIDE-CoVE | T3.3 Circular Economy Skills | Course 3, Module 1
3

## Slide 5
HOW THIS MODULE WORKS
Four sessions, six hours, one outcome
SESSION 1
Construction's
resource footprint
1.5h
The data: who uses what, who emits what
SESSION 2
Linear vs
circular economy
1.5h
Two models. One sustainable. Why it matters
SESSION 3
Policy drivers
1.5h
EU + Ireland: what's required of every site
SESSION 4
Embodied carbon
+ site actions
1.5h
Five things you can do, starting Monday
PRACTICAL OUTPUT: a one-page site handout with climate impacts, key policies, and a circular vs linear chart for your own trade
4

## Slide 6
BEFORE WE START
Six terms you'll hear all module
Get familiar now. The full glossary is in your workbook.
CE
Circular Economy
An economic model where materials and products are kept in use as long as possible — opposite of ‘take-make-waste’.
LCA
Life Cycle Assessment
A method to calculate the environmental impacts of a product across its whole life, from cradle to grave.
EPD
Environmental Product Declaration
A standardised, third-party-verified report showing a product's environmental impact across its lifecycle.
EC
Embodied Carbon
The CO₂ released to make, transport and install a material — before the building is even used.
CSRD
Corporate Sustainability Reporting Directive
EU 2024 directive requiring large companies to publicly report their environmental impact.
GPP
Green Public Procurement
Buying environmentally-better products in the public sector. Ireland: ‘Buying Greener’ strategy.
INSIDE-CoVE | T3.3 Circular Economy Skills | Course 3, Module 1
5

## Slide 7
SESSION 1 OF 4
Construction's Resource Footprint
Why what we build matters for the planet — and for the climate clock • 1.5 hours
5

## Slide 8
SESSION 1 · THE NUMBERS
Construction is the largest industrial sector on Earth
And it has the resource footprint to prove it.
50%
of ALL raw materials
extracted globally
...are used by construction
35%
of the EU's total
waste generation
...comes from construction & demolition
37%
of global
CO₂ emissions
...are linked to construction & buildings
Sources: EU Circular Economy Action Plan (COM 2020/98) · Building a Zero Carbon Ireland (IGBC, 2022)
INSIDE-CoVE | T3.3 Circular Economy Skills | Course 3, Module 1
6

## Slide 9
SESSION 1 · WHERE WE STAND
Five countries, same challenge
Where the INSIDE-CoVE partners stand on construction emissions and circularity.
🇮🇪
Ireland
23 Mt CO₂e/yr
from built environment
37% of national emissions
Lead: TUS
🇩🇪
Germany
120 Mt CO₂e/yr
from built environment
~33% of national emissions
Building law since 2020
🇬🇷
Greece
13 Mt CO₂e/yr
from built environment
~28% of national emissions
EU Just Transition fund
🇪🇸
Spain
65 Mt CO₂e/yr
from built environment
~30% of national emissions
Strong CE plan since 2020
🇨🇾
Cyprus
1.2 Mt CO₂e/yr
from built environment
~22% of national emissions
Small but growing sector
Sources: National GHG inventories (EEA, 2023); IGBC Building a Zero Carbon Ireland (2022); national CE strategies
INSIDE-CoVE | T3.3 Circular Economy Skills | Course 3, Module 1
8

## Slide 10
SESSION 1 · MATERIAL FLOWS
Where does it all go?
The journey of a single tonne of concrete — from quarry to landfill.
01
Extract
Limestone, sand, gravel
from quarries
→
02
Manufacture
Cement burned at
1,450 °C in kilns
→
03
Transport
Truck, ship, train
to site
→
04
Build & Use
50–80 years of
service life
→
05
Demolish
Most ends up
in landfill
THE PROBLEM: at the end, 80% of construction & demolition waste in Europe goes to landfill or low-grade fill — and the cycle starts again at step 01 with virgin materials.
INSIDE-CoVE | T3.3 Circular Economy Skills | Course 3, Module 1
7

## Slide 11
SESSION 1 · WHERE THIS IS GOING
By 2050: a world that won't be the same
URBAN POPULATION GROWTH
+2.75bn
people will move to cities by 2060. They will need housing, schools, hospitals — buildings.
WHAT THIS MEANS FOR CONSTRUCTION
100+ Gt
of embodied carbon from new buildings to 2060 alone
4×
more plastic, 3× more aluminium, 2× more steel and cement by century end
920 Gt
CO₂ just from cement, steel, aluminium, plastic by 2100
$15 trillion
of materials locked into new buildings — a stockpile to be reused
THE WINDOW IS NOW. The choices we make on every site this decade will be locked into the climate for centuries.
Sources: UN World Urbanization Prospects; Material Economics (2018); One Click LCA Embodied Carbon Review
10

## Slide 12
VIDEO RESOURCE · 4 MIN
Watch: What is the Circular Economy?
▶
ELLEN MACARTHUR FOUNDATION
What is the Circular Economy? https://youtu.be/zCRKvDyyHmI?si=Sr-vy1tP-93hHmeR
youtube.com · Duration 3:48 · Subtitles available
WHAT TO LOOK FOR
1
The three principles of the circular economy
2
The difference between biological and technical cycles
3
Why ‘eliminating waste’ is a design choice, not a recycling problem
4
How the model applies to construction
DISCUSS AFTER WATCHING
Which of the principles is hardest to apply on site? Why?
INSIDE-CoVE | T3.3 Circular Economy Skills | Course 3, Module 1
11

## Slide 13
ACTIVITY · 15 MIN
Group
Discussion
Work in pairs or trios
Then share back to the room
Think about your trade
On your last project, what was the one material you saw being wasted most?
01
What was the material, and roughly how much got wasted?
02
Why was it wasted — was it offcuts, damage, or overordering?
03
What would have to change for that waste to be avoided next time?
Facilitator: capture responses on a whiteboard. Look for patterns across trades.
8

## Slide 14
VIDEO RESOURCE · 13 MIN
Watch: Embodied Carbon 101
https://youtu.be/Pugl5aOzqM8?si=wfqd0lrs-Tqmhmwy
▶
AFTER THIS VIDEO YOU WILL KNOW
1
Why embodied carbon now matters as much as operational
2
The relationship between A1–A5 carbon and design decisions
3
What ‘upfront carbon’ means in industry terms
4
Three industry roles: designer, contractor, client
13

## Slide 15
SESSION 1 · WATCH & REFLECT
Video resource
▶
ELLEN MACARTHUR FOUNDATION
The Basics of Circular Economy https://www.youtube.com/live/PkfkMNnRO14?si=VPFvJmrVlD01e5i7
Duration: 45:40 · YouTube · Captions available
AFTER WATCHING
Three reflection questions:
1
What does 'restorative by design' mean in your own words?
2
Name one product or material in your work that already follows circular principles.
3
Where do you see the biggest gap between linear and circular in construction today?
9

## Slide 16
SESSION 2 OF 4
Linear vs Circular Economy
Two ways to build. One is running out of time. The other is the path forward • 1.5 hours
11

## Slide 17
SESSION 2 · THE BIG IDEA
Two models. One is unsustainable.
THE LINEAR MODEL
TAKE
→
MAKE
→
WASTE
Extract raw materials → manufacture products → use them once → throw them away.
WHAT IT ASSUMES
✕ Resources are infinite
✕ Waste disposal is free and harmless
✕ The climate can absorb our emissions
THE CIRCULAR MODEL
DESIGN
→
USE
→
RECOVER
← loop closes — materials cycle back
Design for long life and disassembly → maintain and repair → reuse and recycle. The cycle closes.
WHAT IT BUILDS IN
✓ Resource limits are respected
✓ Waste becomes raw material
✓ Climate impact is reduced at source
KEY DATA: Ellen MacArthur Foundation estimates 45% of climate emissions come from making 'stuff'. Circular economy is essential to closing the gap.
INSIDE-CoVE | T3.3 Circular Economy Skills | Course 3, Module 1
11

## Slide 18
SESSION 2 · THE HIERARCHY
Not all 'circular' is equal
The waste hierarchy ranks circular actions from best (top) to last resort (bottom).
PREVENT
REDUCE
REUSE
RECYCLE
RECOVER
DISPOSE
BEST
WORST
The hierarchy in plain language:
Prevention is always the best option — no waste at all.
Reuse keeps the material's value intact.
Recycling recovers material but loses value.
Landfill loses everything.
12

## Slide 19
SESSION 2 · THE FULL FRAMEWORK
The 9R framework: from refusal to recovery
Beyond the basic waste hierarchy: nine strategies, ranked by circular value retention.
SMARTER USE & MANUFACTURE
HIGHEST VALUE
R0
Refuse
Don't need it? Don't use it.
R1
Rethink
Use product more intensively (sharing, multi-purpose)
R2
Reduce
Use less material per function
EXTEND PRODUCT LIFE
MEDIUM-HIGH VALUE
R3
Reuse
Use again, same purpose
R4
Repair
Fix to maintain function
R5
Refurbish
Restore + upgrade
R6
Remanufacture
Rebuild to as-new
USEFUL APPLICATION
LOWER VALUE
R7
Repurpose
Discarded product, new function
R8
Recycle
Process to get materials back
R9
Recover
Energy from waste
Source: Potting et al. (2017), ‘Circular Economy: Measuring innovation in the product chain’, PBL Netherlands
18

## Slide 20
SESSION 2 · IN PRACTICE
What does this look like on a real site?
DESIGN & PROCURE
Green procurement, design for disassembly, modular & flexible buildings
PRODUCT MANUFACTURE
Recycled content, durable & repairable products, mono-materials
CONSTRUCTION
Off-site fabrication, prevent waste, reuse offcuts, segregate by stream
OPERATION & USE
Maintenance logs, digital records, sharing of space and facilities
RENOVATION
Smart retrofit, imaginative reuse of components, low-carbon upgrades
DEMOLITION
Pre-demolition audits, selective dismantling, sorting and reusing
Adapted from: EPA Resource Waste Management Plan Best Practice Guidelines (2021); Irish Green Building Council (2020)
13

## Slide 21
CASE STUDY · IRELAND
Rediscovery Centre
Ballymun, Dublin
Built using repurposed fittings and non-structural elements salvaged from buildings across Dublin City Council’s housing stock.
It now serves as the National Centre for the Circular Economy in Ireland.
KEY FEATURES
Built almost entirely from materials that would have gone to landfill
⚒
Salvaged timber
from demolished social housing
❐
Reused windows
from refurbished council homes
❖
Repurposed doors
fixtures and ironmongery
▣
Reclaimed bricks
for external facades
☀
Saved tonnes of CO₂
from avoiding new materials
Source: Dublin City Council, DCCAE, Dept of Housing (2018)
14

## Slide 22
SESSION 2 · INTERNATIONAL EXAMPLES
Three buildings, three approaches
Beyond Ireland: how circular construction is being done elsewhere in Europe.
🇳🇱
PARK 20|20
Hoofddorp, Netherlands
An office park designed as a ‘Building as Material Bank’. Every component logged in a material passport — so when the building eventually comes down, every part has a known second life.
APPROACH
Material passports, design for disassembly
🇩🇰
CIRCLE HOUSE
Aarhus, Denmark
60 social housing units, designed so 90% of materials can be reused at end of life. All connections are bolted, not glued, or welded. The first ‘reversible’ housing project at scale.
APPROACH
Bolted connections, reversible joints
🇮🇪
REDISCOVERY CENTRE
Ballymun, Ireland
National Centre for the Circular Economy. Built entirely from materials salvaged from demolished social housing across Dublin City Council’s stock.
APPROACH
Salvaged components, adaptive reuse
20

## Slide 23
VIDEO RESOURCE · 6 MIN
Watch: Building with Circular Economy
▶
ELLEN MACARTHUR FOUNDATION
Circular Construction Explained
Youtube · Duration 5:42
KEY CONCEPTS COVERED
Material passports
Tracking what's in every building
Design for disassembly
Building so it can be taken apart
Modular construction
Building from reusable units
Material banks
Buildings as future supply chains
22

## Slide 24
ACTIVITY · 20 MIN
Spot the
Difference
Individual exercise
Walk-through then group review
Site walk-through (15 min)
Walk through your current or last site (in your head, or on photos). Find five examples — circular or linear.
CIRCULAR examples
LINEAR examples
1.
1.
2.
2.
3.
3.
4.
4.
5.
5.
Then share (10 min): which one would be easiest to improve? Hardest? Why?
15

## Slide 25
SESSION 3 OF 4
Policy Drivers
The rules behind the work: what Europe and Ireland require of every construction site • 1.5 hours
17

## Slide 26
SESSION 3 · THE LAW OF THE LAND
How we got here: a policy timeline
2008
Waste Framework
Directive (EU)
EU sets waste hierarchy
2015
1st Circular Economy
Action Plan (EU)
First major CE push
2019
European Green Deal
(EU)
Net zero by 2050
2020
2nd CE Action Plan
+ Renovation Wave (EU)
Construction targeted
2022
CE Misc. Provisions
Act (Ireland)
First Irish CE law
2024
CSRD reporting
(EU)
Companies must report
WHERE WE ARE NOW: Construction is one of seven priority value chains in the EU's 2020 CE Action Plan. Every site is now affected.
17

## Slide 27
SESSION 3 · WHAT THE EU REQUIRES
Three EU policies in plain language
EU CIRCULAR ECONOMY ACTION PLAN (2020)
WHAT IT DOES
Identifies construction as one of seven priority value chains. Sets targets for recycled content, durability of products, and reduction of construction & demolition waste.
WHAT IT MEANS ON SITE
You will increasingly see specs that require recycled content (e.g. concrete with GGBS, steel with recycled scrap). Material passports for major elements becoming standard.
RENOVATION WAVE (EU, 2020)
WHAT IT DOES
Aims to double the EU's annual renovation rate by 2030. Strong focus on energy efficiency AND circularity together.
WHAT IT MEANS ON SITE
More retrofit and adaptive reuse work — fewer pure demolitions, more upgrades. Selective deconstruction, materials surveys, and reuse planning become standard.
CORPORATE SUSTAINABILITY REPORTING DIRECTIVE / CSRD (2024)
WHAT IT DOES
Large contractors and clients must now publicly report their environmental impact, including emissions, waste, and circular material use.
WHAT IT MEANS ON SITE
Your site records contribute to these reports. Material quantities, transport distances, waste sorting accuracy — all are now traceable data points.
INSIDE-CoVE | T3.3 Circular Economy Skills | Course 3, Module 1
18

## Slide 28
SESSION 3 · THE CPR
The Construction Products Regulation: revised 2024
Why this regulation will change what you can buy and use on a building site.
WHAT IT REQUIRES
Recycled content
Minimum recycled content for cement, steel, plastics in scope
Durability
Minimum service life requirements for major products
Repairability
Products designed so components can be replaced
Environmental declaration
EPDs mandatory for major construction products
CE marking + DoP
Updated to reflect environmental performance
WHAT CHANGES ON SITE
1
Material delivery dockets now include CO₂ data and recycled content %
2
Suppliers must provide EPDs alongside technical data sheets
3
Some products you used last year may not be compliant this year
4
Lower-carbon alternatives become standard, not optional
5
Material passports recommended for major elements
Source: Regulation (EU) 2024/3110 of the European Parliament and of the Council, 27 November 2024 (replaces 305/2011)
INSIDE-CoVE | T3.3 Circular Economy Skills | Course 3, Module 1
26

## Slide 29
SESSION 3 · IRELAND IN FOCUS
Ireland: the national picture
23 Mt
CO₂e/year
from Ireland's built environment
= 37% of national emissions
51%
emissions cut
required by 2030 under Climate Action Plan
Construction is a priority sector
30%
embodied carbon cut
required from construction materials by 2030
Climate Action Plan 2023 target
KEY IRISH POLICIES AFFECTING YOUR SITE
Waste Action Plan for a Circular Economy
2020–2025
Ireland's national waste policy
Circular Economy & Miscellaneous Provisions Act
2022
First Irish law defining CE
Climate Action Plan
2024 (annual)
51% emissions cut by 2030
Green Public Procurement Strategy
2024–2027
Greener purchasing in public sector
INSIDE-CoVE | T3.3 Circular Economy Skills | Course 3, Module 1
19

## Slide 30
SESSION 3 · PARTNER COUNTRIES
Policy snapshot: across the partner countries
Same EU framework, different national flavour.
🇩🇪
Germany
GEG (2020) + KrWG
Building Energy Act mandates lifecycle-based design. KrWG sets C&D recycling rate at 90%. Plus federal Resource Efficiency Programme (ProgRess III).
🇬🇷
Greece
National CE Strategy 2022
Greece's CE Action Plan integrates with Just Transition mechanism. Cement and aggregate recycling targets to 2030. Lagging on implementation but accelerating.
🇪🇸
Spain
España Circular 2030
Comprehensive strategy launched 2020. Material extraction reduction target: 30% by 2030. Strong CDW regulation since 2008 (RD 105/2008).
🇨🇾
Cyprus
Action Plan 2021–2027
Smaller economy, focused CE strategy. CDW management plan since 2015. Tourism-construction overlap creates unique pressures.
INSIDE-CoVE | T3.3 Circular Economy Skills | Course 3, Module 1
28

## Slide 31
SESSION 3 · ON THE GROUND
What's already changing on site?
Five things you have probably already seen — even if you didn't know why.
01
Material delivery dockets now record CO₂ data
Required by CSRD reporting and increasingly by clients.
02
Tighter specs on recycled content
GGBS in concrete, recycled scrap in steel — these are no longer optional in many tenders.
03
Pre-demolition audits become standard
EU Waste Framework Directive requires this on most projects over a certain size.
04
Green Public Procurement (GPP) compliance
Buying Greener Strategy 2024–2027 — apply or explain why you didn't.
05
Material passports / digital logbooks
Tracking what's in the building so it can be reused at end of life.
INSIDE-CoVE | T3.3 Circular Economy Skills | Course 3, Module 1
20

## Slide 32
VIDEO RESOURCE · 2 HOURS TOTAL
Watch: EU Policy Briefing: Circular Economy and Products Everything as a Service & the Circular Economy
▶
INSIDE-CoVE | T3.3 Circular Economy Skills | Course 3, Module 1
31

## Slide 33
ACTIVITY · 10 MIN
Policy
Cards
Pairs · Match cards
Match the policy to its site impact
You'll get a set of cards. Match each policy to the on-site activity it most affects.
EXAMPLE
POLICY
CSRD (2024)
→
SITE IMPACT
Material delivery dockets must now record CO₂
After matching: discuss in pairs which policy will most affect YOUR specific trade in the next 2 years.
21

## Slide 34
SESSION 4 OF 4
Embodied Carbon and Site Actions
Five things you can do — on every site, on every job • 1.5 hours
23

## Slide 35
SESSION 4 · THE KEY CONCEPT
What is embodied carbon?
In plain English:
Embodied carbon is the CO₂ released to make, transport and install a material — before the building is even used.
OPERATIONAL CARBON
CO₂ from USING the building
Heating, cooling, lighting, hot water, plug loads — over the building's life.
Every day, for 50+ years
EMBODIED CARBON
CO₂ from BUILDING it
Extraction, manufacturing, transport, installation, maintenance, demolition.
Locked in at construction
KEY POINT: For a new energy-efficient building, embodied carbon can be 50–80% of its lifetime climate impact. Site decisions matter.
23

## Slide 36
SESSION 4 · THE DATA
Embodied carbon: which materials matter most
Typical embodied carbon (kg CO₂e per kg of material) for common construction materials.
Aluminium (virgin)
12.5 kg CO₂e/kg
Steel (virgin)
2.8 kg CO₂e/kg
Steel (recycled)
0.8 kg CO₂e/kg
Portland cement
0.95 kg CO₂e/kg
Concrete (typ.)
0.13 kg CO₂e/kg
Brick (clay)
0.25 kg CO₂e/kg
Concrete block
0.1 kg CO₂e/kg
Timber (CLT)
0.45 kg CO₂e/kg
Timber (sawn, kiln-dried)
0.2 kg CO₂e/kg
Glass (float)
1.4 kg CO₂e/kg
Plasterboard
0.39 kg CO₂e/kg
Insulation (mineral wool)
1.3 kg CO₂e/kg
KEY INSIGHTS
Aluminium = 12× worse than steel by kg
Recycled steel = 70% lower than virgin
Timber locks carbon in
Concrete blocks beat clay bricks
Insulation: high per kg, low per m²
Source: ICE Database v3.0 (Inventory of Carbon and Energy), University of Bath / Circular Ecology
INSIDE-CoVE | T3.3 Circular Economy Skills | Course 3, Module 1
36

## Slide 37
SESSION 4 · WHAT YOU CAN DO
Five everyday site actions
Things you control. Things that change the outcome. Starting Monday.
01
☑
Order accurately
Overordering is the
single biggest cause
of avoidable waste
02
☂
Protect on delivery
Damaged materials
become waste — not
part of the building
03
♻
Reuse offcuts
Timber, steel, blocks —
offcuts often have a
second use on-site
04
⚘
Choose lower-carbon
Where specs allow:
GGBS over Portland,
recycled over virgin
05
✎
Record your data
EPDs, quantities,
transport distances —
they feed reporting
INSIDE-CoVE | T3.3 Circular Economy Skills | Course 3, Module 1
24

## Slide 38
SESSION 4 · THE IMPACT
Do these matter? The data says yes.
WHAT THE RESEARCH SHOWS
10–20%
of a building's embodied carbon can be reduced through site practice changes alone — without adding to construction cost.
WHERE THE SAVINGS COME FROM
Avoiding overordering
~40%
Reusing offcuts on-site
~25%
Specifying lower-carbon materials
~20%
Better delivery protection
~10%
Improved waste segregation
~5%
Source: UCL Bartlett Institute of Sustainable Heritage; ICE Embodied Carbon Database; Bionova / One Click LCA (2018) The Embodied Carbon Review
INSIDE-CoVE | T3.3 Circular Economy Skills | Course 3, Module 1
25

## Slide 39
SESSION 4 · PLAN OF ACTION
From learning to doing: your site action plan
Fill this in for your next site. One action per row. Set a date.
Action area
What I will do specifically
Who needs to know
By when
01 Order accurately
02 Protect on delivery
03 Reuse offcuts
04 Choose lower-carbon material
05 Record material data
MY SIGNATURE / COMMITMENT
____________________________________
REVIEW IN 30 DAYS
Tick off completed actions. Identify blockers.
38

## Slide 40
VIDEO RESOURCE · 10 MIN
Watch: Cutting Site Waste in Practice
▶
CONSTRUCTION INDUSTRY FEDERATION (CIF) IRELAND
Cutting Site Waste in Practice
youtube.com · Duration 9:30 · Irish site footage and interviews
EXAMPLES YOU'LL SEE
Bricklayer
Cutting from offcut bin first
Plasterer
Mixing only what's needed
Carpenter
Tracking offcuts on a board
Site manager
Daily 5-min waste briefing
Supplier
Take-back agreement for pallets
40

## Slide 41
ASSESSMENT · KNOWLEDGE CHECK
Quick check — 5 minutes
Not graded. This helps you see what's stuck.
Q1
Roughly what percentage of EU waste comes from construction & demolition?
A) 5% B) 15% C) 35% D) 60%
Q2
Which economic model assumes resources are infinite?
A) Circular B) Linear C) Hybrid D) Restorative
Q3
What does 'embodied carbon' refer to?
A) Energy used in heating B) Carbon to make/transport materials C) Tree-stored carbon D) Demolition emissions only
Q4
Which Irish law first defined the circular economy in 2022?
A) Climate Action Act B) CE Misc. Provisions Act C) Waste Framework D) GPP Strategy
Q5
Which is the BEST option in the waste hierarchy?
A) Recycle B) Recover C) Reuse D) Prevent
Answers (don't peek!): Q1: C · Q2: B · Q3: B · Q4: B · Q5: D
26

## Slide 42
PRACTICAL OUTPUT · YOUR DELIVERABLE
Build your one-page site handout
1
Climate impacts
Three key statistics about construction's environmental footprint, written for your trade.
INCLUDE:
• 50% of raw materials extracted globally...
• CO₂ emissions linked to construction...
• Construction & demolition waste in EU...
2
Policy snapshot
Three policies that affect your trade — EU and Irish — in plain language.
INCLUDE:
• EU CE Action Plan: what it requires...
• CSRD: how it affects site records...
• Ireland CE Act: legal obligations...
3
Linear vs Circular chart
A simple visual showing how your trade can move from linear to circular practice.
INCLUDE:
• Linear column: what's done now...
• Circular column: what's needed...
• One example for your specific trade...
SUBMIT BY: End of Module 1 · FORMAT: One A4 page, handwritten or typed · REVIEWED BY: Facilitator, formative only
27

## Slide 43
MODULE 1 · RECAP
What you can now do
✓
Describe the construction sector's resource flows
You now know: 50% materials, 35% waste, 37% CO₂
✓
Distinguish linear from circular models
You can explain both with real examples
✓
Identify policies affecting your trade
EU + Ireland policies, plain language, plain implications
✓
Explain embodied carbon and propose actions
Definition + 5 site actions you control
COMING UP IN MODULE 2: Building lifecycle stages and flows — product, construction, use, end-of-life.
28

## Slide 44
SELF-STUDY · 1 HOUR
Watch on your own time
Eight curated videos. Together they count as 1 hour of self-directed study. Track on the workbook.
▶
9:00
EMF
Circular Economy Detailed
Ellen MacArthur Foundation deeper explainer
▶
11:00
WGBC
Net Zero Buildings 101
World GBC overview of net-zero pathway
▶
8:15
UKGBC
Embodied Carbon Primer
UK GBC introduction with case studies
▶
15:00
IGBC
Building Zero Carbon Ireland
Irish-specific roadmap briefing
▶
12:00
RIBA
Climate Challenge in Construction
Royal Institute of British Architects
▶
7:30
OECD
Material Resource Productivity
OECD on resource efficiency
▶
6:00
BBC
How concrete is destroying the Earth
BBC Reel short documentary
▶
8:45
Vox
The Cement Problem
Vox explainer on cement carbon
44

## Slide 45
MODULE 1 · ESSENTIAL READING
Where to read more
POLICY & STRATEGY
European Commission (2020). A New Circular Economy Action Plan
COM(2020) 98 final
Government of Ireland (2020). A Waste Action Plan for a Circular Economy
National Waste Policy 2020–2025
Government of Ireland (2022). Circular Economy & Misc. Provisions Act
First Irish CE legislation
DECC (2024). Climate Action Plan 2024
Dublin: Government of Ireland
EPA (2024). Buying Greener: GPP Strategy
& Action Plan 2024–2027
European Commission (2020). A Renovation Wave for Europe
COM(2020) 662 final
DATA & TECHNICAL
Bionova / One Click LCA (2018). The Embodied Carbon Review
Materials carbon footprint data
Irish Green Building Council (2022). Building a Zero Carbon Ireland
Built environment decarbonisation
Ellen MacArthur Foundation (2022). Circular Economy in the Built Environment
Definitive CE/construction primer
BRE (2015). The Green Guide to Specification
Material environmental ratings
EU Joint Research Centre. Level(s) framework
EU sustainability reporting for buildings
ICE Embodied Carbon Database. Inventory of Carbon and Energy
Bath University — free dataset
29

## Slide 46
GOING FURTHER
Where to go beyond this module
Free resources, accredited courses, and communities of practice for ongoing learning.
FREE
Self-directed
Online portals and toolkits
Spend an hour a week. Pace yourself.
Ellen MacArthur Foundation Learning Hub
WBCSD Circular Buildings Toolkit
Level(s) Framework user guide (EU JRC)
Irish EPA Circular Economy hub
ICE Embodied Carbon Database
ACCREDITED
Formal courses
Recognised qualifications
Build credentials and progress careers.
INSIDE-CoVE Modules 2–5 (you are here →)
IGBC Home Performance Index Assessor
BREEAM Assessor (BRE Academy)
LEED Green Associate (USGBC)
DGNB Auditor (German Sustainable Building Council)
COMMUNITY
Networks & events
Learn from peers
Don't go it alone. Find your tribe.
Irish Green Building Council (IGBC) member events
Circular Economy Ireland community
Construction Industry Federation events
World Green Building Week (every September)
Sustainability Skills Network (CIF)
46

## Slide 47
MODULE 1 · GO DEEPER
Self-study resources
Self-study on your own time — count as 1 hour of self-directed study. Zero Waste – Building a Sustainable Future through Zero Waste
▶
ELLEN MACARTHUR FOUNDATION
What is the Circular Economy?
3:48 min
Plain-language intro to CE for any audience.
▶
WORLD GREEN BUILDING COUNCIL
Bringing Embodied Carbon Upfront
12:30 min
How embodied carbon works — animated.
▶
UK GREEN BUILDING COUNCIL
Net Zero Carbon Buildings
8:15 min
Operational vs embodied carbon explained.
▶
IRISH GREEN BUILDING COUNCIL
Building a Zero Carbon Ireland
15:00 min
Ireland-specific data and case studies.
30

## Slide 48
MODULE 1 · SELF-CHECK
Before you move on...
Tick each box honestly. If you can't tick all five, revisit the relevant session.
I can quote at least one statistic for construction's resource use or emissions
I can explain the difference between linear and circular economy in 30 seconds
I know what the EU Circular Economy Action Plan says about construction
I can define embodied carbon and explain why it matters
I can name three actions on my next site that will reduce embodied carbon
✓ All five ticked? You are ready for Module 2: Building Lifecycle Stages and Flows
31

## Slide 49
END OF
Module 1
Why Lifecycle Matters
MODULE COMPLETE
Six hours of content. Four sessions. One handout.
WHAT'S NEXT
1. Submit your Practical Output
2. Complete the self-check (slide 47)
3. Begin Module 2: Lifecycle Stages and Flows